## Slide 1
2nd Journal review
Clinical application of
SHG microscope
2015/10/13 M2 Atsuta

## Slide 2
① M. Weinigel et al.,“Compact clinical high-NA multiphoton endoscopy”, Proc. of SPIE.8217, 821706-1(2012).
② H. G. Breunig et al. , “Combining multiphoton and CARS microscopy for skin imaging”, Proc. of SPIE.8588, 85880N-1(2013).
③ M. Weinigel et al., “A novel clinical multimodal multiphoton tomograph for AF, SHG,CARS imaging, and FLIM”, Proc. of SPIE.8948, 89481R-1(2014).

## Slide 3
Introduction
SHG microscope : observation of non-centrosymmetric molecules (e. g. collagen)
⇒ Selective and non-invasive
・ Compact & Portable system
・ Combination with other microscope
To Clinical application…
Ref.) http://www.jenlab.de/DermaInspect.29.0.html
DermaImspect
(Jen Lab.)

## Slide 4
① Compact clinical high-NA multiphoton endoscopy
Ref.) http://www.jenlab.de/DermaInspect.29.0.html
Clinical high-resolution multi-tomography apparatus
Large probe ⇒ Restrict external access possibilities
hard-to-reach areas (like wounds)
It can be improved by the clinical multiphoton endoscopy.
Using gradient index (GRIN) lenses
& combining multiphoton endoscopy
(Fluorescent & SHG)
based on with CE-marked clinical tomography

## Slide 5
Setup

## Slide 6
Results
The lateral resolution : 0.87 μm
The axial resolution : 5.5 μm

## Slide 7
Fluorescence (green)
SHG (yellow)
in vivo imaging @ Depth-resolved
12 optical sections
@ steps of 13 μm.
It demonstrates that
high contrast features can be imaged up to a depth of about 117 μm.
Sample:
Human skin (forearm)

## Slide 8
Summary
・Development of a set-up aimed at a combination of microscopic endoscope and medical certification tomography
・High resolution image has been acquired is in vivo multiphoton image human skin from the above depth 100μm

## Slide 9
② Combining multiphoton and CARS microscopy for skin imaging
What’s CARS microscopy ?
Multiphoton microscope + CARS microscopy
Ω=2845
The stretching vibration energy of CH2
Biological measurement…
known for lipids

## Slide 10
Setup
Notes: CARSアプリケーションのスーパーコンティニュームデバイス
- 800nmの範囲のFSポンプ用に最適化
- CARSのために適したデュアル出力ピーク
- エンドファセットビーム拡大

## Slide 11
Results
7.4 s/frame for images
with 512 x 512 pixels
(FOV :200 x 200 μm)
Pump : 800nm
Stokes : 1035nm
CARS : 652nm
Stratum spinosum
Notes: 2845c𝑚^(−1)でCH2の振動を励起するのに800 nmのポンプパルスでは1035 nmのCARSストークスパルスが必要であり，652 nmでCARS信号を生成
汗腺を含む皮膚の領域を図2.4に示す．皮膚表面から約18μmの深さである．図2.4a,bはそれぞれ，TPF/SHGとCARSイメージを示している．この領域は有棘層でケラチンがほとんど含まれていない．汗腺を含む領域周辺の細胞が可視化されており，霧のようなイメージはCH2含有分子，おそらく脂質によるものであると考えられる．CARSポンプおよびストークスパルスなしの場合のTPF/SHGイメージ(図2.4c)，およびCARSイメージ(図2.4d)

## Slide 12
SHG & CARS イメージ
Notes: 図2.5aにはSHG発生コラーゲン構造を含むことが知られている乳頭層を示している．コラーゲンSHG信号が見え，TPF/SHGチャネルで支配的である．CARSチャネルでは異なった強度分布が見られる．強度分布がコラーゲンの構造に従って見られるが，領域のほとんどに分布している．CARSの先行研究では，コラーゲンやエラスチン構造(動脈組織など)からは，2845 c𝑚^(−1)の信号が出ると報告されているが，図2.5bからは，コラーゲンやエラスチン以外の分子(ここでは脂質分子)

## Slide 13
Summary
・Clinical CARS / TPF / SHG multi-photon human skin in vivo imaging of the imaging system has been shown.
・Different fluorophores and CH2 molecular distribution was observed inside the deeper layers of the skin cell structure and elastin or collagen are present.

## Slide 14
③ A novel clinical multimodal multiphoton tomograph
for AF, SHG,CARS imaging, and FLIM
Conventional system
Ref.) http://www.horiba.com/jp/
medical certification tomography
combination AF / SHG / CARS microscope
elastin, melanin, and NAD(P)H
⇒ fluorescence lifetime
imaging (FLIM)

## Slide 15
Setup

## Slide 16
Results

## Slide 17
Results
healthy human skin @ a depth of 70 μm (dermal papillae)
FLIM : Melanin has a strong short lifetime component (orange color coded)
and elastin longer lifetimes (blue-green color coded)

## Slide 18
Summary
・Multiphoton tomography, based on autofluorescence and SHG, to allow tissue imaging of high resolution.
・Additional information about the non-fluorescent and non-SHG-active tissue component can be obtained by CARS.
・New and it is compact, multi-channel simultaneous detection, AF · FLIM, separation of the SHG and CARS signal has become possible.

## Slide 19
Summary
These are expected to be a very powerful tool for the skin test in the future of the medical field and cosmetic field.
Multiphoton microscope is compact, and built into clinical high-resolution multi-tomograph, and the observation field is spread by combining with other systems.

## Slide 20
That’s all.